Spike encoding Notes
General info:
- Each encoding serves as a unique way to extract information from the input signal.
- Selecting the appropriate encoding method depends on the signals characteristics like presence of relevant information in time or frequency domain as well as noise. It also depend on how the encoding change the data characteristics.

Intro:
Why did we chose this paper and why this paper is important?
- Having many recent papers about spike encoding indicates that this is still an active area of investigation which lots of unanswered questions
- It gives an overall upate about the current state of spike encodings and what improvement has this area had in recent years.
- It leaves some many fundamental questions to answer and it suggests future direction of the field

Rate Coding (Definition)
When a feature is presented, a neuron fires with a rate monotonically to the intensity or saliency of that feature. This model works well with stimuli that vary slowly in time, since the noisiness of spikes requires integration over some time window. Rate code was the base of hubel and wiesel model (cat experiment to different stimuli orientation).

Count Rate:
- Counting the number of spikes and divide the number of spike by the duration of the stimulus.
- To evaluate the rate you have measure single neuron for single trial and average over time. The measures interval should be long enough because the noisiness of spikes requires integration over long time window
- Temporal averaging can work well in cases where the stimulus is constant or slowly varying and does not require a fast reaction of the organism
- Slow and not biologically plausible

Density Rate:
- Define short time window deltaT, Count across all trials with the same time interval
- Will give a peri-stimulus-time Histogram (PSTH)
- Rate measure with a temporal resolution (division by deltaT)
- PSTH requires several trials to build up, not the code used in the brain
- PSTH relies on the implicit assumption that there are always populations of neurons with similar properties
- The stimulus needs to be presented again and again
- Way too slow and not biologically plausible
Population Coding:
- The rate in this case is the population average
- It records over a population of neurons using the same stimilus on a single trial
- Postsynaptic neuron is driven by the population activity
- Take into account that the populations of neuron will always have a certain degree of heterogeneity both in their internal parameters and in their connectivity pattern

Limitation of Rate code
- In order to get rid of the noise and arrive at a reliable estimate of the rate, the experimenter has to average over a larger number of spikes which that the rate accuracy is proportional with the number of spikes generated
- Temporal averaging can work well in cases where the stimulus is constant or slowly varying and does not require a fast reaction of the organism
- The image projected onto the retinal photoreceptors changes every few hundred milliseconds - and with each new image the retinal photo receptors change the response, due to the saccade. Therefore, a postsynaptic neuron does not have the time to perform a temporal average over many (noisy) spikes
- PSTH needs several trials to build up
- PSTH measuring the firing rate can make sense only if there are large populations of similar neurons that receive the same stimulus
- PSTH relies on the implicit assumption that there are always populations of neurons with similar properties
  - Consider for example a frog which wants to catch a fly. It can not wait for the insect to fly repeatedly along exactly the same trajectory. The frog has to base its decision on a single run – each fly and each trajectory is different.
- Population rate assumes neurons are homogeneous with identical connection. However, real populations will always have a certain degree of heterogeneity both in their internal parameters and in their connectivity pattern

Temporal Coding (Definition)
By definition, temporal coding is a type of neural coding which relies on precise timing of action potentials or inter-spike intervals. It tries to account for short-term stimuli producing a small number of spikes

Threshold-based representation:
Advantages:
- Simple and fast (see code)
- Reduce white noise by applying the threshold to small perturbations in the signal
- No falsely registered values at the start or end of neither the spike train nor the reconstructed signal

Disadvantages:
- Sensitive to strong white noise in the signal resulting in strong low-frequency artifact components
- Tradeoff between representing small and large events. Since the whole sample length is considered for threshold value calculation, this encoding can be disadvantageous for long samples where there may be amplitude differences between events of different parts of the sample

Step forward:
Advantages:
- The threshold can be chosen such that small and large amplitude events are both well represented
- Noise in the signal is minimally reduced by the threshold
- Due to the moving baseline, the reconstructed signal does not drift away even for longer signals (No overshoot)

Disadvantages:
They haven’t reported any disadvantage elsewhere

Moving window:
Advantages:
- It is robust against white noise
- Moving averge is an optimal smoothing filter in the time domain against white noise
- Could be used to filter out a strong, artifact frequency component, e.g., power line noise in EEG signals
Disadvantages:
- But it is a poor low pass filter in the frequency domain
- Window size heavily affect the cutoff frequency, the slope of the frequency response ad the noise reduction
- The signal beginning is not encoded well until the window size is reached, therefore it requires tricks to adjust the baseline
- Overshoot-type errors often appear
Ben’s spike algorithm encoding:
Advantages:
- BSA is an algorithm for producing the spike train from which the original signal can be reconstructed well
- Decoding is straightforward and simple: a convolution of the spike train with the filter coefficients gives the reconstructed signal
- BSA can be applied to any positive-valued signal if the filter coefficients are scaled up such that they appropriately match the signal boundaries

Disadvantages:
- Filter design is based on two parameters: cutoff frequency and filter size
- Cutoff frequency is to be chosen based on the task-relevant frequency spectrum
- BSA works only for positive-valued signals
- The original BSA encoding requires input with [0, 1] limits

Correlation and Synchrony (Definition)
(I) It uses the temporal reference to other spiking neurons. (II) Information is encoded by the distinction of which neurons fire at the same time. (III) where a subset of neurons inside a population is active at any given point of time. (IV) Enables to represent a virtually infinite number of patterns without significant errors. (V) It was observed in the somatosensory cortex of monkeys, visual cortex of cats as well as grid and place cells.

Synchrony is more like a measure of the degree of synchrony between spike trains and it can be called inversely spike train distances. It can be used (I) to quantify the reliability of neuronal responses upon repeated presentations of a stimulus and (II) or to test the performance of neuronal models.

- Synchrony between a pair or many neurons could signify special events and convey information which is not contained in the firing rate of the neurons
- Neurons work in synchrony firing with different relative delays might signify a different stimulus resulting in a coincidence detector
- SPIKE synchronization act as coincidence detectors and quantify the degree of similarity or dissimilarity between as few as two spike trains

Sparse distribution representations (Sparse coding)
Example of sparse coding is Dropout and HTM

What is sparse coding?
- Information is represented by a relatively small number of simultaneously active neurons out of a large population
- In many sensory nervous systems neurons at later stages of processing are generally less than active than those at earlier stages. For instance, a neuron in the retina responds to whatever contrast is present at that point in space, whereas a neuron in the visual cortex would respond only to a specific spatial configuration of light intensities (e.g. an edge of a particular orientation).

Advantages:
- It represents complex data in a way that is easier to read out at subsequent levels of processing
- It allows for increased storage capacity in associative memories
- It makes the structure in natural signals explicit
- It saves energy – Power efficient
Disadvantages:

Parallel binary coding
Advantages:
Disadvantages:

Conclusion:
What are the main take aways from this study?
- What should we focus on as a next step? Simpler spike encoder that solve simple tasks or more complex spike encoder for more complex tasks?
- Should a spike encoder replicate biology or be inspired by biology (inspiration vs replication)
- Based on what criterias someone should select a specific encoding technique?
- What are some aspects which we can compromise /sacrifice while selecting any encoding scheme ?
- Should we always compare different encoding techniques for every problem? If so, how?
- What kinds of investigation that need to be made (authors suggested further investigation but what kind of investigation as this is too broad)